## Slide 1: C1: Intro to ARM NEON
(These slides assume the ARMv7 NEON Architecture)

## Slide 2: Coprocessors
A coprocessor is an auxiliary processing element operating under the direction of the primary CPU.
Certain processor-intensive tasks can be offloaded to the coprocessor to improve overall system performance.
A coprocessor may be used for tasks such as:
  Floating-point operations
  Graphics processing
  Cryptographic processing
  I/O processing
A coprocessor may operate synchronously with the primary CPU or may be independent processors operating asynchronously

## Slide 3: Quick introduction to SIMD
SIMD stands for Single Instruction Multiple Data Stream
The idea is that a single CPU instruction will be executed but multiple instances of that operation will be executed on different pieces of data.
For example, say you wanted to add all the elements in one array to all the elements of another array and store them in a third array.
For(int i = 0; i < 10; i++)
c[i] = a[i] + b[i];
Since each of these additions occur independently from on another we may be able to execute them in parallel

## Slide 4: Quick introduction to SIMD
If we are able to load multiple array values from memory at the same time and have an architecture that supports SIMD operations we could potentially speed up the entire computation.
For example, consider that the arrays a, b, c all contain single bytes, arranged in memory like this
a[0], a[1] …
Assume we have thirty-two bit registers:
  Load 4 values from array into register R0
  Load 4 values from array B into register R1
  Add each of the four elements from R0 to the four elements in R1 and store the result in a third register (R2)
  Store values of R2 into array c.
  This is shown in the next slide

## Slide 5: Quick introduction to SIMD
a[0] | a[1] | a[2] | a[3]
+ | + | + | +
b[0] | b[1] | b[2] | b[3]
↓ | ↓ | ↓ | ↓
c[0] | c[1] | c[2] | c[3]
R0
R1
R2
A single add instruction is dispatched that performs four independent additions treating the 32-bit registers as separate 8-bit values.

## Slide 6: ARM’s NEON coprocessor
The NEON coprocessor implements the Advanced SIMD media processing architecture. Advanced SIMD is an optional part of the ARMv7-A architecture. The components of the NEON coprocessor are:
  NEON register file with 32x64-bit general-purpose registers
  NEON integer execute pipeline (ALU, Shift, MAC)
  NEON dual, single-precision floating-point execute pipeline (FADD, FMUL)
  NEON load/store and permute pipeline

## Slide 7: ARM NEON code development
Developing code for NEON, or any SIMD architecture, typically involves an additional layer of complexity.
As a programmer, there are several ways you can use Neon technology:
  Neon intrinsics (these look like function calls in C/C++ but turn into specific Neon assembly instructions upon compilation)
  Neon-enabled libraries (a set of functions implemented in Neon assembly)
  Auto-vectorization by your compiler (the most “automatic” way to use Neon)
  Hand-coded Neon assembler (leads to good performance but is labor intensive.)

## Slide 8: ARM NEON code development
The 32 64-bit NEON registers are labeled D0, D1, … D31
They can be combined in pairs to create 128-bit registers.
  D0 and D1 map to Q0
  D2 and D3 map to Q1, …
These registers can be treated as vectors

## Slide 9: ARM NEON data processing
NEON data processing instructions include a suffix to indicate the type and size of data being manipulated.
VADD.I16 Q0, Q1, Q2
  Each 128-bit Q-register is being treated as 8 16-bit signed integers. The addition will take place like this:
Q1[0] | Q1[1] | Q1[2] | Q1[3] | Q1[4] | Q1[5] | Q1[6] | Q1[7]
+ | + | + | + | + | + | + | +
Q2[0] | Q2[1] | Q2[2] | Q2[3] | Q2[4] | Q2[5] | Q2[6] | Q2[7]
↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓
Q0[0] | Q0[1] | Q0[2] | Q0[3] | Q0[4] | Q0[5] | Q0[6] | Q0[7]

## Slide 10: ARM NEON data processing
VSUB.U8 D0, D1, D2
  Each 64-bit D-register is being treated as 8 8-bit unsigned integers. The subtraction will take place like this:
D1[0] | D1[1] | D1[2] | D1[3] | D1[4] | D1[5] | D1[6] | D1[7]
– | – | – | – | – | – | – | –
D2[0] | D2[1] | D2[2] | D2[3] | D2[4] | D2[5] | D2[6] | D2[7]
↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓ | ↓
D0[0] | D0[1] | D0[2] | D0[3] | D0[4] | D0[5] | D0[6] | D0[7]

## Slide 11: ARM NEON loads and stores
The simplest example of a load:
  VLDR D0, [R0] – load 64 bits starting at the address in R0 into NEON register D0
For 128 bits we simply use one of the Q registers
  VLDR Q1, [R0]
VSTR is the comparable store instruction.
NEON also provides sophisticated loads and stores that can de-interleave data as it’s loaded or only modify parts of NEON registers. One can also load multiple registers at once.
  VLD 1.1

## Slide 12: ARM NEON code examples
Show some NEON instructions and their SISD equivalents

## Slide 13: References
https://developer.arm.com/architectures/instruction-sets/simd-isas/neon
https://developer.arm.com/documentation/ddi0344/k/neon-and-vfp-programmers-model/about-the-neon-and-vfp-programmers-model/neon-media-coprocessor
https://elinux.org/images/4/40/Elc2011_anderson_arm.pdf
http://www.add.ece.ufl.edu/4924/docs/arm/ARM%20NEON%20Development.pdf
http://download.xskernel.org/docs/processors/cortex-a53/neon_tutorial.pdf

## Slide 14: Questions
What is SIMD, and how does it improve performance?
  Multiple arithmetic operations can take place in parallel.
  This can reduce the total number of clock cycles required to complete a computation
What is the “cost” of developing code for NEON?
  Increased code complexity may lead to code that is more difficult to maintain
  Development time is increased.

## Slide 15: Lab
Goals:
  Find insight into how a SIMD enabled co-processor can speed up certain kinds of algorithms.
  Observe the design/complexity vs. speed tradeoffs that SIMD development entails.
General Idea
  You are given a simple test harness to run and time three different versions of vector addition.
  A linear C-code version and a linear assembly version are provided for you.
  You will write two versions the vectorized algorithm using ARM’s NEON instructions.