## Slide 1: CUDA
Notes: Previous CUDA slides have some more questions if this was presented in reading first (in F18, it was all lecture since the book didn’t cover CUDA…)
Last question (syncthreads) not really fair without reading; need to know that each syncthreads line is a separate barrier

## Slide 2: GPGPU programming (General-Purpose Graphics Processing Unit)
Graphics processing requires many similar operations in “graphics pipeline”
  Triangles going through rotation and scaling, shading, and texturing
Graphics Processing Units (GPUs) develop to meet this need and then get converted for general purpose programs
CUDA (Compute Unified Device Architecture) is a GPU design and extension of C (et al) to support GPGPU programming developed by Nvidia
  Market share leader; leading open alternative is OpenCL

## Slide 3: Programming model: Memory
Program mainly runs on “Host” (= CPU), but can call functions on “Device” (= GPU)
Host and Device have separate address spaces (at least historically)
  Memory must be explicitly transferred

## Slide 4: Programming model: Processing
GPU can run many threads simultaneously, but not independently
  Device threads connected in groups called warps
  All members of a warp perform the same operation
    SIMD = Single Instruction, Multiple Data
Programmer writes function to run on device (kernel)
Invokes it with a number of blocks and threads (per block)
All these threads run the function
  Use implicit arguments blockIdx and threadIdx to identify itself

## Slide 5: Logistics: Compiling and running CUDA programs
Compiling:
nvcc -o hello hello.cu
Running:
./hello
Compiler; really a wrapper for gcc or another C compiler
Name of the source code. CUDA files use the extension .cu
-o flag: Used to specify the executable to create

## Slide 6: “Hello World” for CUDA
#include <stdio.h>
__global__ void hello() {
int id = threadIdx.x + blockIdx.x * blockDim.x;
printf("Hello from thread %d (%d of block %d)\n", id, threadIdx.x, blockIdx.x);
}
int main() {
hello<<<3,4>>>(); //launch 3 blocks of 4 threads each
cudaDeviceSynchronize(); //make sure kernel completes
}

## Slide 7: “Hello World” for CUDA
#include <stdio.h>
__global__ void hello() {
int id = threadIdx.x + blockIdx.x * blockDim.x;
printf("Hello from thread %d (%d of block %d)\n", id, threadIdx.x, blockIdx.x);
}
int main() {
hello<<<3,4>>>(); //launch 3 blocks of 4 threads each
cudaDeviceSynchronize(); //make sure kernel completes
}
Device code (runs on GPU)

## Slide 8: Possible output
Hello from thread 0 (0 of block 0)
Hello from thread 1 (1 of block 0)
Hello from thread 2 (2 of block 0)
Hello from thread 3 (3 of block 0)
Hello from thread 8 (0 of block 2)
Hello from thread 9 (1 of block 2)
Hello from thread 10 (2 of block 2)
Hello from thread 11 (3 of block 2)
Hello from thread 4 (0 of block 1)
Hello from thread 5 (1 of block 1)
Hello from thread 6 (2 of block 1)
Hello from thread 7 (3 of block 1)
Out of order; blocks are executed separately and in any order

## Slide 9: Overview of a CUDA program
In host code:
  Allocate memory on device
  Copy data to device
  Kernel call
  Copy results to host
  Free device memory
In device code:
  __global__
  determine thread ID
  bounds check

## Slide 10: Adding vectors using CUDA (Not actually fast…)
Take 2 input arrays and add index-wise to produce output array
2
5
3
1
0
6
5
3
2
0
4
1
7
8
5
1
4
7
+
=

## Slide 11: Adding vectors using CUDA (Not actually fast…)
int main() {
int* a; //first input array (on host)
int* a_dev; //first input array (on device)
a = (int*) malloc(N*sizeof(int));
cudaMalloc((void**) &a_dev, N*sizeof(int));
… //same for b and res
free(a);
cudaFree(a_dev);
}
In host code:
  Allocate memory on device
  Copy data to device
  Kernel call
  Copy results to host
  Free device memory
In device code:
  __global__
  determine thread ID
  bounds check

## Slide 12: Adding vectors using CUDA (Not actually fast…)
int main() {
…
cudaMemcpy(a_dev, a, N*sizeof(int), cudaMemcpyHostToDevice));
…
cudaMemcpy(res, res_dev, N*sizeof(int), cudaMemcpyDeviceToHost)
…
}
In host code:
  Allocate memory on device
  Copy data to device
  Kernel call
  Copy results to host
  Free device memory
In device code:
  __global__
  determine thread ID
  bounds check

## Slide 13: Adding vectors using CUDA (Not actually fast…)
int main() {
…
int threads = 512; //# threads per block
int blocks = (N+threads-1)/threads;
//# blocks (N/threads rounded up)
kernel<<<blocks,threads>>>(res_dev, a_dev, b_dev);
…
}
In host code:
  Allocate memory on device
  Copy data to device
  Kernel call
  Copy results to host
  Free device memory
In device code:
  __global__
  determine thread ID
  bounds check

## Slide 14: Adding vectors using CUDA (Not actually fast…)
__global__ void kernel(int* res, int* a, int* b) {
//sets res[i] = a[i] + b[i]
//each thread is responsible for one value of i
int thread_id = threadIdx.x + blockIdx.x*blockDim.x;
if(thread_id < N) {
res[thread_id] = a[thread_id] + b[thread_id];
}
}
In host code:
  Allocate memory on device
  Copy data to device
  Kernel call
  Copy results to host
  Free device memory
In device code:
  __global__
  determine thread ID
  bounds check

## Slide 15: Threads and blocks
int threads = 512; //# threads per block
int blocks = (N+threads-1)/threads; //# blocks (N/threads, rounded up)
kernel<<<blocks,threads>>>(res_dev, a_dev, b_dev);
Why use more than a single block?
  Limited number of threads per block (depends on card being used)
Why not use N blocks?
  Threads in block share variables (__shared__) and have barrier (__syncthreads())
  Also, technically limited (w/ newer cards, the limit is 231 – 1)

## Slide 16: Threads and blocks
int threads = 512; //# threads per block
int blocks = (N+threads-1)/threads; //# blocks (N/threads, rounded up)
kernel<<<blocks,threads>>>(res_dev, a_dev, b_dev);
Why use more than a single block?
  Limited number of threads per block (depends on card being used)
Why not use N blocks?
  Not as fast: blocks are split into warps, which run simultaneously
  Threads in block share variables (__shared__) and have barrier (__syncthreads())
  Also, technically limited (w/ newer cards, the limit is 231 – 1)

## Slide 17: Linearizing multi-dimensional arrays
cudaMemcpy only transfers 1D arrays
need to represent 2D array:

## Slide 18: Linearizing multi-dimensional arrays
cudaMemcpy only transfers 1D arrays
need to represent 2D array:
cell (x, y)
cell y*row_length + x

## Slide 19: Linearizing multi-dimensional arrays
cudaMemcpy only transfers 1D arrays
need to represent 2D array:
cell (x, y)
cell y*row_length + x
Consider cell with 1D coordinate i:
What is the coordinate of the cell below it?
What expression tests if it is on the right edge?

## Slide 20: Linearizing multi-dimensional arrays
cudaMemcpy only transfers 1D arrays
need to represent 2D array:
cell (x, y)
cell y*row_length + x
Consider cell with 1D coordinate i:
What is the coordinate of the cell below it? i + row_length
What expression tests if it is on the right edge? i % row_length == row_length – 1